## Slide 1
APPLIED MACHINE LEARNING · PHASE 1 PROJECT PRESENTATION
Turbofan Engine Remaining Useful Life Prediction
Predicting cycles left before failure from engine sensor history · NASA C-MAPSS FD001 turbofan dataset
Keshav · Rohit Kumar · Mayank Yadav · Arun · Sarvesh Kumar
1 THE PROBLEM
RUL = last cycle − current cycle
Example: engine fails at cycle 240, now at cycle 180
180 flown
60
240 − 180 = 60 cycles of life remain
Our goal is to predict how many cycles an engine has left from its sensor history, so maintenance can be planned before failure.
Target capped at 125 cycles: healthy engines look alike.
2 THE DATASET
20,631
training rows
100 engines
13,096
test rows
100 engines
26
columns
incl. 21 sensors
0
missing values
0 duplicate rows
One row = one engine at one operating cycle.
Training engines run to failure, so RUL labels can be calculated.
Test engines stop early; true RUL is supplied separately.
Chart: Lifetime (cycles)
| 120-160 | 160-200 | 200-240 | 240-280 | 280-320 | 320-360 | 360-400
Engines | 16 | 38 | 29 | 9 | 5 | 2 | 1
Engines fail anywhere between 128 and 362 cycles (mean 206), so RUL cannot be read from the cycle count alone; it must be inferred from sensor trends.
Fig. 1 Lifetime of the 100 training engines (cycles).
Notes: RUL is the number of cycles left before failure. Training engines run to failure, so we can compute it; test engines stop early and NASA gives the true RUL separately. Lifetimes vary from 128 to 362 cycles, so engine age alone cannot tell us the RUL.

## Slide 2: Exploration: which sensors carry the degradation signal?
Engine 1 of the training set and all 100 training engines, using RUL computed from each engine’s final cycle.
Chart: Operating cycle
Fig. 2 Sensor change vs. cycle 1, engine 1: one flat, three drifting.
Chart: 
| s11 | s4 | s15 | s2 | s17 | s3 | s8 | s13 | s9 | s14 | s20 | s21 | s7 | s12
Correlation with RUL | -0.7 | -0.68 | -0.64 | -0.61 | -0.61 | -0.58 | -0.56 | -0.56 | -0.39 | -0.31 | 0.63 | 0.64 | 0.66 | 0.67
Fig. 3 Correlation of each retained sensor with RUL (all training rows).
WHAT THE DATA SHOWS
7 flat sensors removed: s1, s5, s6, s10, s16, s18, s19.
One operating condition: settings dropped, no normalisation needed.
No missing values or duplicates in 20,631 rows.
Sensors 4 and 11 rise and sensor 12 falls as failure nears.
Strongest links (|r| ≈ 0.7): s11, s4, s12, s7. Sensors s9 and s14 are weak.
Flat sensors carry no signal. The 14 retained sensors drift with wear but are noisy, so single readings are not enough: trend features are needed.
Notes: Fourteen sensors remain after removing the seven flat ones. Temperatures and pressures such as s11 and s4 rise towards failure, while s7, s12, s20 and s21 fall. Because single readings are noisy, we build trend features next.

## Slide 3: Feature engineering: measuring drift from a healthy start
Rolling statistics over the last 10 cycles of the same engine (current and past readings only). Example: sensor 11, engine 1.
Chart: Operating cycle
Fig. 4 Raw reading vs. 10-cycle rolling mean (sensor 11).
Chart: Operating cycle
Fig. 5 Drift of sensor 11 from engine 1’s own first-10-cycle level.
THE 71 INPUT FEATURES
71
= 1 cycle + 14 raw sensors + 14 × 4 rolling statistics
Mean: recent average level.
Std. deviation: recent variability.
Slope: direction of change.
Drift (_dev): mean minus the engine’s own healthy start.
Window = current + previous 9 cycles; a truncation test proves no future readings leak in.
The drift features carry about 84 % of the Random Forest’s importance, and s11_dev alone about 74 %: comparing each engine with its own healthy start exposes wear that raw readings hide.
Notes: For every sensor we compute four features over the last 10 cycles. The most useful one turned out to be drift from healthy: how far a sensor has moved from that engine's own normal level in its first 10 cycles.

## Slide 4: Methodology: models and validation design
Same features, same engine-based split and same validation engines for every model.
1 Load & check
2 Cap RUL at 125
3 Split by engine
4 Build features
5 Tune models
6 Test once
FOUR REGRESSION MODELS
MODEL | FAMILY | HOW IT WORKS
Baseline | Reference | Always predicts the average training RUL.
Linear Regression | Linear (OLS) | Weighted sum of standardised features.
Decision Tree | Single tree (CART) | Yes/no splits on features; pruned (depth 12, min. leaf 50).
Random Forest | Tree ensemble | Averages 150 trees grown on bootstrap samples.
VALIDATION DESIGN
80
20
engines to train
engines to validate
3-fold GroupKFold tuning · 100 official test engines
RMSE = √ mean (actual − predicted)²
MAE = mean |actual − predicted|
R² = share of RUL variation explained
Errors are in cycles; RMSE penalises large errors more.
Splitting by engine (never by row) keeps each engine out of both training and validation; settings are tuned on the 80 training engines only, and the test set is used once at the end.
Notes: Whole engines go to training or validation, never both, to avoid leakage. Settings are tuned with GroupKFold on the 80 training engines; the 20 validation engines pick the best model; the official test set is used only once at the end.

## Slide 5: Results: Random Forest gives the lowest error
Scores on the 100 official NASA test engines, in operating cycles; lower is better.
Chart: 
| Baseline | Linear Regression | Decision Tree | Random Forest
MAE | 34.83 | 12.84 | 10.8 | 8.27
RMSE | 41.94 | 15.85 | 14.96 | 11.44
Fig. 6 Test MAE and RMSE for the four models (100 official engines).
SCORECARD
MODEL | VAL RMSE | TEST MAE | TEST RMSE | TEST R²
Baseline | 41.72 | 34.83 | 41.94 | -0.10
Linear Regression | 15.29 | 12.84 | 15.85 | 0.84
Decision Tree | 14.13 | 10.80 | 14.96 | 0.86
Random Forest | 10.34 | 8.27 | 11.44 | 0.92
INTERPRETATION
Random Forest: lowest test RMSE (11.44), about 28% below Linear Regression.
All three models beat the baseline (RMSE 41.94) by about 3 to 4 times.
68 of 100 test engines predicted within 10 cycles; 89 within 20.
Validation and test errors are close for every model (Random Forest RMSE 10.34 vs 11.44), so the engine-based validation was a trustworthy guide to real performance.
Notes: Random Forest was chosen on validation before touching the test set. On the 100 official test engines it reaches RMSE 11.44, MAE 8.27 and R squared 0.92, against RMSE 41.94 for the always-predict-the-average baseline.

## Slide 6: Error analysis, conclusions and next steps
Where do the large errors come from, and how much do the engineered features help? Validation engines, all three models.
Chart: True RUL band (cycles)
| 0–25 | 25–50 | 50–75 | 75–100 | 100–125 | >125
Linear Reg. | 13.93 | 21.87 | 20.81 | 13.26 | 12.34 | 12.2
Decision Tree | 5.88 | 13.7 | 22.8 | 21.67 | 15.12 | 7.67
Random Forest | 4.25 | 8.33 | 15.43 | 16.75 | 11.7 | 6.37
Fig. 7 Validation RMSE by true-RUL band: errors peak at 50–100 cycles left.
Chart: 
| Linear Reg. | Decision Tree | Random Forest
Raw sensors only | 17.37 | 17.73 | 15.98
Engineered features | 15.29 | 14.13 | 10.34
Fig. 8 Validation RMSE, raw sensors vs. engineered features.
CONCLUSIONS
Engineered features cut validation RMSE by 12% (Linear), 20% (Tree) and 35% (Forest).
Hardest region: 50–100 cycles left, when wear is just appearing.
Early life looks easy partly because of the 125-cycle cap.
Limits: FD001 only, simulated data, one split.
NEXT STEPS
1
Extend to the multi-condition subsets FD002–FD004.
2
Repeated cross-validation and uncertainty ranges.
3
Phase 2: compare with LSTM / CNN on the same split.
Classical ML with good degradation features predicts engine RUL to within about 8 cycles on average.
Notes: Answer to the research question: yes. Engineered features reduce the Random Forest error by 35 percent. The hardest region is the transition from healthy to degrading, 50 to 100 cycles before failure. Phase 2 will compare deep learning under the same protocol.

## Slide 7: Team introduction
Each member owned one stage of the shared project pipeline.
EDA & baseline
Rohit Kumar
Feature engineering
Mayank Yadav
Decision Tree & app
Arun
Random Forest
Keshav
Documentation
Sarvesh Kumar
ENROLLMENT NO. | NAME | ROLE / CONTRIBUTION
2401010392 | Rohit Kumar | Data exploration: checked data quality, plotted sensor trends, screened flat sensors; fixed the linear model and final comparison.
2401010271 | Mayank Yadav | Data preparation: built the capped RUL target, engine-wise split and the 71 rolling and drift features.
2401010098 | Arun | Modelling: tuned and pruned the Decision Tree, ran the final comparison and built the Streamlit web app.
2401010221 | Keshav | Random Forest (best model): grid-searched and trained the 150-tree forest, analysed feature importance, raw vs. engineered features and early/late-life errors, and evaluated it on the test set.
2401010422 | Sarvesh Kumar | Documentation: wrote the academic report, viva Q&A and README with setup instructions and results.
Notes: Introduce each team member and their part of the pipeline. Thank the audience and invite questions.