## Slide 1
APPLIED MACHINE LEARNING · PHASE 1 PROJECT
Remaining Useful Life Prediction for Turbofan Engines
How many flights does an engine have left? Sensor feature engineering with classical ML on NASA C-MAPSS FD001
100
engines recorded until failure
71
engineered input features
10.14
test RMSE in cycles (XGBoost)
Team: Rohit Kumar · Mayank Yadav · Arun · Sarvesh Kumar · Keshav
Notes: Introduce the project: predicting remaining useful life (RUL) of turbofan engines from sensor data, using classical machine learning only. Headline result: XGBoost predicts the official NASA test engines with an RMSE of 10.14 cycles.

## Slide 2: The task: predict cycles left before failure
A regression problem on 100 run-to-failure engines and 100 truncated test engines
1
WHAT IS RUL?
RUL = last cycle − current cycle
Example: engine fails at cycle 240, today is cycle 180
180 flown
60
RUL = 60 cycles
Healthy engines look alike, so the target is capped at 125 cycles for every model.
2
THE DATA
20,631
training rows
13,096
test rows
21
sensors per row
0
missing values
Each row = one engine at one cycle: id, cycle, 3 settings, 21 sensors.
Chart: Engine lifetimes (cycles)
| 120-160 | 160-200 | 200-240 | 240-280 | 280-320 | 320-360 | 360-400
Engines | 16 | 38 | 29 | 9 | 5 | 2 | 1
Fig. 100 training engines fail after 128-362 cycles.
Notes: RUL is simply the number of cycles left. Training engines run to failure, so we can compute it; test engines stop early and NASA gives the true RUL separately. Lifetimes vary a lot, so age alone cannot tell us the RUL.

## Slide 3: Which sensors show engine wear?
Correlation of each useful sensor with RUL over all 20,631 training rows
Chart: 
| s11 | s4 | s15 | s2 | s17 | s3 | s8 | s13 | s9 | s14 | s20 | s21 | s7 | s12
Correlation with RUL | -0.7 | -0.68 | -0.64 | -0.61 | -0.61 | -0.58 | -0.56 | -0.56 | -0.39 | -0.31 | 0.63 | 0.64 | 0.66 | 0.67
Fig. Negative = value rises as failure nears; positive = value falls.
WHAT WE FOUND
7 sensors never change (s1, s5, s6, s10, s16, s18, s19): removed
One operating condition: no normalisation needed
Strongest signals: s11, s4, s12, s7 (|r| ≈ 0.7)
s9 and s14 are weak: each engine has its own offset
Sensors are noisy and flat while healthy. Trends over several cycles matter more than a single reading.
Notes: Fourteen sensors remain after removing flat ones. Temperatures and pressures such as s11 and s4 rise towards failure, while s7, s12, s20, s21 fall. Because single readings are noisy, we build trend features next.

## Slide 4: Turning noisy readings into wear signals
Four features per sensor from the last 10 cycles of the same engine (past and current cycles only)
Chart: Engine 1, sensor s11 (HPC static pressure)
Fig. The rolling mean removes noise and reveals the upward drift.
1
Rolling mean
Average of last 10 readings: removes noise
2
Rolling std
How much the sensor jumps: instability
3
Rolling slope
Best-fit line slope: direction and speed of change
4
Drift from healthy
Mean minus the engine's own first-10-cycle level
71 features = cycle + 14 raw sensors + 14 × 4 engineered. A truncation test proves no future data is used.
Notes: For every sensor we compute four features over the last 10 cycles. The most useful one turned out to be drift from healthy: how far a sensor has moved from that engine's own normal level in its first 10 cycles.

## Slide 5: Fair comparison: same features, same engine split
Every model is tuned and judged on engines it has never seen
1
Load & check
2
Cap RUL at 125
3
Split by engine
4
Build features
5
Tune models
6
Test once
FOUR REGRESSION MODELS
Model | Type | How it works
Baseline | Reference | Always predicts the average RUL
Random Forest | Tree ensemble | Averages many decision trees
XGBoost | Boosted trees | Each new tree fixes earlier errors
Elastic Net | Linear + penalty | Weighted sum; weak features set to 0
VALIDATION DESIGN
80
engines train
20
engines validate
3
GroupKFold folds
100
test engines
Metrics: RMSE (big misses count more), MAE (average miss), R²
Notes: Whole engines go to training or validation, never both, to avoid leakage. Settings are tuned with GroupKFold on the 80 training engines; the 20 validation engines pick the best model; the official test set is used only once at the end.

## Slide 6: Results: XGBoost is about 7 cycles off on average
RMSE in cycles, lower is better; validation = 20 held-out engines, test = 100 official NASA engines
Chart: 
| Baseline | Random Forest | XGBoost | Elastic Net
Validation RMSE | 41.72 | 10.34 | 9.6 | 15.04
Test RMSE | 41.94 | 11.44 | 10.14 | 16.13
Fig. Validation and test errors are close, so the engine split was a reliable guide.
SCORECARD
Model | Val RMSE | Val MAE | Test RMSE | Test MAE
Baseline | 41.72 | 36.93 | 41.94 | 34.83
Random Forest | 10.34 | 6.77 | 11.44 | 8.27
XGBoost | 9.60 | 6.05 | 10.14 | 7.40
Elastic Net | 15.04 | 12.01 | 16.13 | 13.14
INTERPRETATION
XGBoost wins; Random Forest is close (≈1 cycle)
Both tree models are ~4× better than the baseline
Elastic Net misses the curved wear pattern
Notes: XGBoost was chosen on validation before touching the test set. On the 100 official test engines: RMSE 10.14, MAE 7.40, R squared 0.94. Random Forest is only about one cycle worse, so we call XGBoost slightly better.

## Slide 7: Features cut the error by over a third
Validation RMSE with raw sensors only vs with engineered features, and error by life stage
Chart: 
| Random Forest | XGBoost | Elastic Net
Raw sensors only | 15.98 | 15.53 | 17.96
Engineered features | 10.34 | 9.6 | 15.04
Fig. 35-38% lower error for the tree models.
EARLY VS LATE LIFE (VALIDATION)
Model | RMSE: >100 left | RMSE: ≤100 left
XGBoost | 7.33 | 11.45
Random Forest | 8.01 | 12.26
CONCLUSIONS
Yes: engineered features clearly help classical ML
Drift from the healthy level is the strongest feature
Errors grow near failure; early life looks easy only because of the 125 cap
Limits: FD001 only, simulated data, one split
NEXT STEPS
Extend to multi-condition sets FD002-FD004
Repeated cross-validation and uncertainty ranges
Phase 2: compare with LSTM / CNN on the same split
Notes: Answer to the research question: yes. Engineered features reduce the tree models' error by 35 to 38 percent. The hardest region is the transition from healthy to degrading. Phase 2 will compare deep learning under the same protocol.

## Slide 8
Our team
Student name | Enrollment number | Email
Rohit Kumar | 2401010392 | rohit.kumar2024@nst.rishihood.edu.in
Mayank Yadav | 2401010271 | mayank.yadav2024@nst.rishihood.edu.in
Arun | 2401010098 | arun.2024@nst.rishihood.edu.in
Sarvesh Kumar | 2401010422 | sarvesh.kumar2024@nst.rishihood.edu.in
Keshav | 2401010221 | keshav.2024@nst.rishihood.edu.in
Thank you · Questions?
Notes: Introduce each team member. Thank the audience and invite questions.